## Slide 1
Image Contrast Adjustment using Nvidia Performance Primitives (NPP)
Yang Song

## Slide 2: Outline
NPP Introduction
Problem Statement
Solution and Result
Further Reading/Resources

## Slide 3: What is NPP?
A library of GPU-accelerated image, signal and video processing functions.
Key features:
  Arithmetic and Logical Operations
  Statistical Operations
  Filter Functions, etc.
Performance
  5x ~ 10x than CPU-only implementation.
Amount
  Around 4000 in CUDA 5.0.

## Slide 4: Problem Statement
Hazy source image lacks contrast.
Adjustment algorithm (8-bit image):
  Offset and scale image, such that darkest pixel is mapped to 0 and brightest pixel is mapped to 255
Three operations needed:
  MinMax, Subtract and Multiply
Good News!
NPP has them all 

## Slide 5: Solution
Load image on host
Output the image.
Copy image from host to GPU
Call nppiMinMax, nppiSubC, nppiMulC
Transfer result
back to host
You have to fill in
this part.

## Slide 6: NPP Image Representation
145 145 143 145 147 142 141 134 131
146 148 146 146 146 145 139 140 143
145 149 146 145 144 146 142 139 130
147 147 149 146 145 146 133 128 119
145 143 143 145 143 145 136 137 121
136 137 132 131 131 132 128 121 110
155 157 155 158 157 156 154 140 146
158 156 159 158 158 157 155 149 120
pSrc
nSrcStep
oROI
pSrc
with offset
Image is represented by two parameters:
  pSrc: pointer to the first pixel of the image
  nSrcStep: number of bytes between successive rows
Notes: Explain the image data storage. The first pixel of the image. Line stride in bytes.

## Slide 7: Function Naming
nppiMulC_8u_C1IRSfs
  npp
  i: image module (s: signal module)
  MulC: primitive name (Add, Sum, etc.)
  8u: data type of the image (16u, 32s, 32f, 64f, etc.)
  C1: single channel (C3R, C4R, AC4R, etc.)
  I: in-place (out-of-place if not specified)
  R: work on ROI (region of interest)
  Sfs: allow result scaling

## Slide 8: Read Image
145 145 143 145 147 142
146 148 146 146 146 145
145 149 146 145 144 146
147 147 149 146 145 146
145 143 143 145 143 145
136 137 132 131 131 132
155 157 155 158 157 156
158 156 159 158 158 157
Host (CPU)
pSrc_Host
Device (GPU)
nHeight
nWidth
145 145 143 145 147 142
146 148 146 146 146 145
145 149 146 145 144 146
147 147 149 146 145 146
145 143 143 145 143 145
136 137 132 131 131 132
155 157 155 158 157 156
158 156 159 158 158 157
pSrc_Dev
nHeight
nWidth
nSrcStep_Dev
cudaMemcpy2D

## Slide 9: NPP scratch buffer
nppiMinMax_8u_C1R needs device buffer
  NPP does not allocate memory internally (unbeknownst to the user).
  Offer users max control and flexibility on memory management.
  Buffer can be reused to improve performance and avoid device-memory fragmentation .

## Slide 10: nppiMinMaxGetBufferHostSize_8u_C1R
Parameter list:
  NppiSize oSizeROI  oROI
  int * hpBufferSize  &nBufferSize_Host
Notes: Encourage them to look up the manual.

## Slide 11: nppiMinMax_8u_C1R spec
Parameter list:
  const Npp8u * pSrc  pSrc_Dev
  int nSrcStep  nSrcStep_Dev
  NppiSize oSizeROI  oROI
  Npp8u * pMin  pMin_Dev
  Npp8u * pMax  pMax_Dev
  Npp8u * pDeviceBuffer  pBuffer_Dev
Notes: Encourage them to look up the manual.

## Slide 12: Integer-Result Scaling (Part 1)
Avoid the clamping loss on the integer data (especially on 8u and 16u images).
Parameter "nScaleFactor" controls the amount of scaling:
Example: nppsSqr_8u_Sfs()
  , clamped to 255.
  Pass scale factor 8: final result = , which will be rounded to 254.

## Slide 13: nppiSubC_8u_C1RSfs spec
Shift minimum pixel value to 0.
nppiSubC_8u_C1RSfs
  const Npp8u * pSrc  pSrc_Dev
  int nSrcStep  nSrcStep_Dev
  const Npp8u nConstant  nMin, nMax, 255
  Npp8u * pDst  pDst_Dev
  int nDstStep  nDstStep_Dev
  NppiSize oSizeROI  OROI
  int nScaleFactor  0
Notes: Take SubC as an example. Explain the scale factor here. Explain the 8u_C1RSfs. Use two nppi instead of three. Try to combine the two MulC and DivC together.

## Slide 14: Multiplication Step
Scale range to [0, 255].
Problem: nppiMulC_8u_C1IRSfs uses a single Npp8u integer as the constant multiplier, but
If multiply by 2 (nearest integer to actual value) error is 0.318182 (i.e. >30%!!!).
Solution: Integer result scaling!
Notes: Take SubC as an example. Explain the scale factor here. Explain the 8u_C1RSfs. Use two nppi instead of three. Try to combine the two MulC and DivC together.

## Slide 15: Integer-Result Scaling (Part 2)
Reduce error using Integer-Result Scaling:
  Express exact multiplier (2.318182) as fraction of the form
  Where n is an integer and s is the integer-scale factor.
With s=6 we get =64.
Difference with exact value 2.318182-2.3125 0.005681 which is close to the 8-bit pixel quantization error (1/255 0.003921).

## Slide 16: Computing optimal nScaleFactor
int nScaleFactor = 0;
int nPower = 1;
while(nPower * 255.0f / (nMax_Host - nMin_Host) < 255.0f)
{
nScaleFactor ++;
nPower *= 2;
}

## Slide 17: nppiMulC_8u_C1IRSfs spec
nppiMulC_8u_C1IRSfs
  const Npp8u nConstant  computed
  Npp8u * pSrcDst  pDst_Dev
  int nDstStep  nDstStep_Dev
  NppiSize oSizeROI  oROI
  int nScaleFactor  computed

## Slide 18: Result
before
after

## Slide 19: Further Reading/Resources
NPP is freely available as part of the CUDA Toolkit at www.nvidia.com/getcuda.
Source code samples demonstrating use of the NPP library:
  Box Filter with NPP
  Histogram Equalization with NPP
  FreeImage and NPP Interoperability
  Image Segmentation using Graphcuts with NPP

## Slide 20: Thank you. Q&A